## Slide 1
SCHOOL OF TECH TRG
ELECTRONICS WING
Notes: .

## Slide 2
SCHOOL OF TECH TRG
DIGITAL COMN
Notes: .

## Slide 3: DIGITAL COMN
ANALOG SIGS
CONTINUOUS
DIFF VALUES IN A LIMITED RANGE AT A PARTICULAR INSTANT OF TIME
EG - VOICE

## Slide 4
DIGITAL SIGS :- THE TYPE OF SIGS WHICH HAVE ONLY TWO DISCRETE VALUES OR LEVELS LIKE HIGH AND LOW OR ZERO AND ONE FOR THE DATA BEING TRANSMITTED DURING ANY PARTICULAR INSTANCE OF TIME .
eg - CALCULATOR, MICRO PROCESSOR.
DIGITAL COMN

## Slide 5: ADV OF DIGITAL OVER ANALOG
EASIER CCTS AS ONLY TWO LEVELS.
ALL TYPES OF MUX POSSIBLE.
HAVE CAPABILITY OF MEMORY HENCE USED IN CMPTRS.
LESS CHANCES OF ERRORS OVER LONG DISTANCE i-e ATTENUATION DO NOT HAVE MUCH EFFECT.

## Slide 6
LATEST ELEC SYS MOSTLY DIGITAL.
RUGGED i.e MORE IMMUNE TO CHANNEL NOISE.
CAN BE EASILY CODED.
IMMUNITY TO NOISE AS ONLY PRESENCE
AND ABSENCE OF SIGS ARE SENSED.
REPEATING FACILITY EXISTS FOR
REGENERATION.
INTERFACE WITH CMPTRS IS POSSIBLE.
EASE OF ACHIEVING SECRECY.
LOW ERROR RATES DUE TO ERROR DETECTION.
ADV OF DIGITAL OVER ANALOG

## Slide 7
ELEMENTS OF A DIGITAL COMMUNICATION SYSTEM

## Slide 8
PROCESS OF DIGITAL COMN
SAMPLING
QUANTISATION
ENCODING
ANALOG SIG
DIGITAL SIG

## Slide 9
PULSE MODULATION
ANALOG
DIGITAL
PULSE AMP MOD (PAM)
P WIDTH MOD (PWM)
(PPM)PULSE
POSN MOD
PCM
DELTA MOD
PTM
IT IS USED TO CONVERT ANALOG SIG INTO BINARY VALUES

## Slide 10
PULSE MODULATION

## Slide 11: PULSE AMPLITUDE MODULATION

## Slide 12: PULSE WIDTH MODULATION
SYMMETRICAL PWM
LEADING EDGE PWM
TRAILING EDGE PWM
MODULATING SIG

## Slide 13: PULSE POSITION MODULATION

## Slide 14: PULSE CODE MODULATION
SAMPLING :- THE PROCESS OF DIVIDING A SIG INTO TIME INTERVALS i.e THE SAMPLING RATE.
SAMPLING THEOREM :- IF THE SAMPLING RATE OF ANY PULSE MODE SYS EXCEEDS TWICE THE MAX OF THE SIG FREQ THE ORIG SIG CAN BE RECONSTRUCTED IN THE RECEIVER WITH MINIMUM DISTORTION.
fs 2 f(DATA SIG)
NOTE-USED FOR DETERMINING MIN SAMPLING RATE.

## Slide 15: BINARY AND PULSE CODE

## Slide 16: SAMPLING
In signal processing, sampling is the reduction of a continuous signal to a discrete signal. A common example is the conversion of a sound wave (a continuous signal) to a sequence of samples (a discrete-time signal). A sample is a value or set of values at a point in time and/or space.

## Slide 17: QUANTIZATION
IT IS THE PROCESS OF ASSIGNING THE SAMPLE VALUE TO A NEAREST QUANTIFIABLE LEVEL . EACH OF THIS QUANTIFIABLE LEVELS IS ASSIGNED A FINITE NO OF CODES.

## Slide 18: QUANTIZATION

## Slide 19: ENCODING
THE PROCESS OF ASSIGNING CODE TO THE QUANTIFIABLE LEVEL OF THE INPUT SIGNAL. THUS THE SIGNAL IS CONVERTED INTO BINARY CODES.

## Slide 20: ENCODING

## Slide 21: QUANTISATION NOISE
IF THE ACTUAL SIGNAL IS COMPARED TO QUANTISED SIGNAL, IT IS SEEN THAT QUANTISATION PROCESS INTRODUCES SOME DISTORTION ,THIS DISTORTION IS KNOWN AS QUANTISATION NOISE.

## Slide 22: DELTA MODULATION
IT IS A PROCESS OF MODULATION WHERE A SERIES OF FIXED WIDTH PULSES IS TRANSMITTED , WHOSE POLARITY INDICATES WHETHER PRESENT INPUT SIG SAMPLE IS LARGER OR SMALLER THAN THE PREVIOUS SIGNAL SAMPLE.

## Slide 23
CONVERTING DECIMAL TO BINARY
1. DIVIDE THE DECIMAL NUMBER SUCCESSIVELY BY UNTIL THE QUOTIENT IS ZERO.
2. NOTE WHETHER EACH REMAINDER IS 0 OR 1.
3. THE REMAINDERS OF 0 AND 1 ARE DIGITS IN THE BINARY NUMBER.
132 = 6 WITH REMAINDER OF 1
6 2 = 3 WITH REMAINDER OF 0
3 2 = 1 WITH REMAINDER OF 1
1 2 = 0 WITH REMAINDER OF 1
13 = 1 1 0 1
DECIMAL TO BINARY

## Slide 24: BINARY TO DECIMAL
1101 = 1X2 + 0X2 + 1X2 + 1X2
= 1 + 0 + 4 + 8
= 13
0
1
2
3

## Slide 25
ASCII CODES.
  AMERICAN STD CODES FOR INFO INTERCHANGE.
BINARY TO DIGITAL .
DIGITAL TO BINARY .

## Slide 26: ERROR DETECTION & CORRECTION
BY ADDING REDUNDANT BIT.
PARITY CHECK CODING.

## Slide 27: PARITY CHECK CODING
TO ADD A SINGLE BINARY DIGIT TO EACH MSG FOR SPECIFIED LENGTH SO THAT OUTPUT OF THE DATA IS EVEN OR ODD . THE ADDED REDUNDANT BIT IS CALLED AS PARITY CHECK BIT .
IN THIS ONLY DETECTION OF ERRORS IS POSSIBLE.

## Slide 28: BOOLEAN ALGEBRA AND LOGIC GATES
A
B
A.B =Y
Y
A B Y
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 29
BULB
S 2
S 1
V
(a) CCT
A
B
A.B =Y
(b) LOGIC SYMBOL
AND GATE

## Slide 30
OR GATE
S1
S2
BULB
V
A
B
A+B =Y
(A)
( B)

## Slide 31
OR GATE
OUT PUT
Y
0
1
1
1
A
B
0
0
1
1
0
1
0
1
INPUT

## Slide 32
NOT GATE
Y
A
A Y
Y=A 0 1
1 0

## Slide 33
NOR GATE
A
B
A B Y
0 0 1
0 1 0
1 0 0
1 1 0
Y
Y=A+B

## Slide 34
NOR GATE
A+B = Y
OUT PUT
INPUTS
A
0
0
1
1
B
0
1
0
1
Y
1
0
0
0
A
B

## Slide 35
X-OR GATE
A B Y
0 0 0
0 1 1
1 0 1
1 1 0
Y=A + B
A
B
Y

## Slide 36
EX NOR ( X NOR)
A
+
B = Y
OUT PUT
INPUTS
A
0
0
1
1
B
0
1
0
1
Y
1
0
0
1
Odd
Odd
Even

## Slide 37
GATE
AND
NOT
NAND
OR
NOR
XOR
XNOR
SYMBOL
INPUT
OUTPUT
ALL 1
ANY 0
1
0
ALL 1
ANY 0
ALL 0
ANY 1
ALL 0
ANY 1
EVEN IS
ODD IS
ODD IS
EVEN IS
1
0
0
1
0
1
0
1
1
0
0
1
0
1
OUT
IN
OUT
IN
OUT
IN
OUT
IN
OUT
IN
OUT
IN
OUT
IN